## Slide 1
Hello
Hej
Hallo
你好
こんにちは
Ciao
Bonjour
Shen
10/17/2024
Notes: Hello everyone, welcome to my trial lecture.
I try to say hello in your mother tongue.
If your mother tongue is, unfortunately, not listed here.
You may give a complaint at the end of this lecture.

## Slide 2
I
2017-2019
Birth
Master
(Technical University of Denmark)
Doctor
(The University of Tokyo)
2020-2023
1995
Self-Introduction: Shen
Notes: I am your lecturer /ˈlek(t)SHərər/. My name is Shen. I am a Ph.D. in Aeronautics and Astronautics.
This slide gives my self-introduction. I was born in 1995.
In 2017, I started my master’s program at DTU in Denmark. At that time, I was studying in automation and robotics.
The left figure was our autonomous driving team at DTU.
After graduating from DTU, I came to Japan for a doctoral program in Aeronautics and Astronautics.
The charming figure on the right is the university of Tokyo.
My research focus in Tokyo was the drone controller design.

## Slide 3
Drone-based
control systems
10/17/2024
Ph.D. in Aeronautics and Astronautics
Shen
Notes: Today’s lecture is about the drone-based control systems.
Specifically, we will control a quadrotor by a pid controller.

## Slide 4
Table of Contents
Quadrotors and Dynamics
Controller Design
Summary
I
II
III
4
13
18
Page
Notes: We will visit the quadrotor and its dynamics first.
After that, we will control this quadrotor with a PID controller before we make a final summary.

## Slide 5
I
The direction of the thrust is adjustable.
Ryll, Markus, Heinrich H. Bülthoff, and Paolo Robuffo Giordano. "Modeling and control of a quadrotor UAV with tilting propellers." 2012 IEEE international conference on robotics and automation. IEEE, 2012.
Tilt-rotor
Quadrotor
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
4
Quadrotors and Dynamics
Notes: There are different kinds of quadrotors.
What you see on the left is a conventional quadrotor.
The direction of the thrust is upward.
On the right, we can see a tiltrotor.
(play the demo)
Different from the conventional quadrotor,
in a tiltrotor, the direction of the thrust is adjustable during the flight.

## Slide 6
I
Quadrotor
The total control force can be produced only in one direction.
Tiltrotor
Tilted-rotor
Based on the trajectories, the optimal structure can be designed.
It is mechanically possible to change the structure of the tiltrotor.
5
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
Quadrotors and Dynamics
Notes: Three relevant drones are listed here.
A conventional quadrotor can produce the total force only in one direction.
That is upward.
A tiltrotor can change its structure.
Therefore, a tiltrotor can change the direction of the thrust during the flight.
The third drone is called the tilted-rotor.
The tilted-rotor cannot change its structure.

## Slide 7
I
Quadrotor
The total control force can be produced only in one direction.
Tiltrotor
Tilted-rotor
Based on the trajectories, the optimal structure can be designed.
It is mechanically possible to change the structure of the tiltrotor.
6
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
Quadrotors and Dynamics
Notes: Today, we will control the conventional quadrotor.
As we mentioned, this quadrotor has four inputs.

## Slide 8
I
7
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
Inputs
Inputs (4) < DoF (6)
We cannot stabilize all the 6 DoF independently.
DoF
Quadrotors and Dynamics
Notes: These 4 inputs are the magnitudes of the 4 thrusts.
F1, F2, F3, F4, respectively.
On the other hand, there are 6 degrees of freedom.
They are roll, pitch, yaw, x, y, and z.
Note that the number of the inputs is less than the number of the degrees of freedom.
Therefore, these 6 DoF cannot be controlled simultaneously or independently.

## Slide 9
I
8
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: Let’s see a simple example here.
A drone is hovering at its initial position.
And it is expected to move to a goal position.
Someone may believe the drone can move without changing the attitude while moving.

## Slide 10
I
8
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: Like this.

## Slide 11
I
8
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics

## Slide 12
I
8
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: Unfortunately, this is not true.
The roll and pitch cannot be zero while moving.

## Slide 13
I
9
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: In contrast, the quadrotor has to change its attitude.

## Slide 14
I
9
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: By adjusting the roll and pitch, the quadrotor will generate the lateral force.

## Slide 15
I
9
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: And this lateral force pushes it horizontally.

## Slide 16
I
9
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics

## Slide 17
I
9
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
We cannot stabilize all the 6 DoF independently.
initial
goal
Quadrotors and Dynamics
Notes: And finally making it reach the goal.

## Slide 18
I
10
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
initial
goal
DoF
Inputs (4) < DoF (6)
We cannot stabilize all the 6 DoF independently.
Quadrotors and Dynamics
Notes: So, the next time your boss is asking you, “Why cannot the drone maintain the zero Euler angles while moving?”
You may reply, “The number of the inputs is less than the number of the degrees of freedom.”

## Slide 19
I
11
Quadrotor
The total control force can be produced only in one direction.
https://www.mathworks.com/matlabcentral/fileexchange/48052-simulate-quadrotor-in-simulink-with-simmechanics
Ryll, M., Bülthoff, H.H. and Giordano, P.R., 2012, May. Modeling and control of a quadrotor UAV with tilting propellers. In 2012 IEEE international conference on robotics and automation (pp. 4606-4613). IEEE.
Rajappa, S., Ryll, M., Bülthoff, H.H. and Franchi, A., 2015, May. Modeling, control and design optimization for a fully-actuated hexarotor aerial vehicle with tilted propellers. In 2015 IEEE international conference on robotics and automation (ICRA) (pp. 4006-4013). IEEE.
initial
goal
DoF
Inputs (4) < DoF (6)
We cannot stabilize all the 6 DoF independently.
Quadrotors and Dynamics
Notes: With only 4 inputs in total,
we will control roll, pitch, yaw, and altitude independently.
To control this quadrotor, we will check its dynamics first.

## Slide 20
I
12
DoF:
Inputs:
Dynamics
Note:
Quadrotors and Dynamics
Notes: What you see on this slide are the dynamic equations of a quadrotor.
I know there are lots of variables.
But don’t be scared.
When you see the complicated equations,
You may observe the inputs and outputs first.
The inputs are the four thrusts, F1, F2, F3, and F4, respectively.
They are here.
The outputs are 6 degrees of freedom.
Phi, theta, psi, X, Y, Z.
Here are the outputs.
This is the dynamics of a quadrotor.
These equations tell us how these degrees of freedom respond to the inputs in a quadrotor.
And we will control this quadrotor after linearizing these dynamic equations.

## Slide 21
II
13
Controller Design
DoF:
Inputs:
Dynamics (after linearization)
initial
goal
Linearize at
Notes: Linearize the dynamics at this equilibrium.
With the small angle approximation, we receive these relationships.
Focus on the result on the left.
The inputs are the four thrusts, F1, F2, F3, and F4.
The outputs are the four degrees of freedom.
They are the altitude, Z, the roll, pitch, yaw angles.
So, these 4 degrees of freedom are controlled independently by the inputs.
Now, let’s check the other part of the linearization.
Focus on the result on the right.
We also color the inputs and outputs.
But wait.
Where are the inputs?
There are no inputs in the equations on the right.
It means that the position is coupled with the attitude.
You may remember, the attitude cannot be zero while the drone moves.
These two equations explain this phenomenon.
We cannot control all 6 degrees of freedom independently.
Actually, these two equations between the attitude and the position are widely used in the setpoint tracking problem.

## Slide 22
IV
Linearize at
Shen Z, Ma Y, Tsuchiya T. Feedback linearization-based tracking control of a tilt-rotor with cat-trot gait plan. International Journal of Advanced Robotic Systems. 2022;19(4). doi:10.1177/17298806221109360
II
quadrotor
14
Controller Design
The Coupled Position and Attitude
Notes: Having this conventional relationship, we can control the position X and Y depending on the attitude.
The figure on the right is from a publication in the quadrotor control.
As we can see, the independent degrees of freedom to be directly controlled are the attitude and altitude.
The position X and Y are controlled by the coupling relationship between the position and the attitude.
In short, we will control the attitude and altitude directly.
And in this first lecture, we will learn how to stabilize the altitude.

## Slide 23
II
15
Altitude Control
Controller Design
Notes: To make the altitude control,
let’s focus on this dynamic equation after linearization.
To make our deduction easier,
we simplify this equation by assigning the right side as u1.
And, we will design the PID controller relying on this dynamic equation.

## Slide 24
II
16
Altitude Control (PID controller)
P I D
Proportional
Integral
Derivative
P I D
Controller Design
Notes: Delta z in this dynamic equation is the difference between the desired altitude and the actual altitude.
If you read the literatures, delta Z is sometimes called the state error.
Our goal is to let Z be equal to Z reference.
In other words, we need to find the input u1,
This u1 will finally make delta Z to be zero.
Here, we introduce a PID controller.
The PID controller is the abbreviation of proportional, integral, and derivative controller.
The Proportional part is the delta Z.
The Integral part is the integral of delta Z.
The Derivative part is the derivative of delta Z.
And a PID controller is the linear combination of the Proportional, Integral, and Derivative part.
The sum is the input of the quadrotor. The quadrotor will be maneuvered by this u1.

## Slide 25
II
17
Altitude Control (PID controller)
P I D
Goal: 5 m
Initial: 0 m
Lift the quadrotor from 0 meter to 5 meters.
MATLAB
Simulink
https://github.com/HansOersted/trial_lecture
Controller Design
Notes: Let’s use this PID controller to stabilize the quadrotor.
Assume a quadrotor is hovering at 0 meter.
And, it is desired to reach the goal at 5 meters.
We will use the PID controller on the right.
The coefficients, Kp, Ki, Kd are specified below.
On the top, you can check the final input.
To demonstrate the behavior of this controller,
I built the simulator in MATLAB.
For the interested researchers, this is the github link.
If you open this link,

## Slide 26
https://github.com/HansOersted/trial_lecture
Notes: You will get access to the simulator on my github.
I recommend my students to download and play with it after the lecture.
If you do so and open my simulator,

## Slide 27
https://github.com/HansOersted/trial_lecture
Controller
Dynamics
Notes: You will see this Simulink file.
It is the digital twin of the quadrotor.
The dynamic equations we saw earlier were constructed here.
And the controller, the PID controller, was built here.
In short, we will use the PID controller to stabilize the quadrotor in this simulator.
Let’s visualize the result.

## Slide 28
II
18
Altitude Control (PID controller)
P D
https://github.com/HansOersted/trial_lecture
The Altitude of The Quadrotor
Controller Design
Notes: On the left, we will see the animation of the quadrotor.
The altitude of the quadrotor will be plotted on the right.
(play the video)
In the simulator,
the drone lifts from 0 to 5 meters as expected.
It means that our PID controller works!
I recommend you to change the coefficients in our controller.
For example, you may change the Kp to another value instead of 1.0 and check the result.
By doing so, you may find some interesting behaviors of the PID controller.
And please write to me if you have these experiences after this class.

## Slide 29
III
19
Summary
What you have learned today
Quadrotor
The total control force can be produced only in one direction.
Dynamics
How the 6 DoF are influenced by the inputs.
Independent DoF
The controller can only stabilize 4 DoFs independently. They are roll, pitch, yaw, and altitude.
Notes: I’ll summarize what we have learned today.
Firstly, the quadrotor was introduced.
We then analyzed the dependencies between the degrees of freedom.
Next, we talked about how these degrees of freedom were influenced by the inputs.
That is the dynamics of the quadrotor.
With the dynamics of the quadrotor, we developed a controller.

## Slide 30
III
20
Summary
What you have learned today
Altitude control
The altitude of the quadrotor is stabilized by a PID controller.
PID controller
PID controller is proportional- Integral-derivative controller.
P:
I:
D:
Notes: A PID controller in specific, to stabilize the quadrotor.
We use this PID controller to make the altitude control.

## Slide 31
III
21
What you will learn…
Attitude control
How to stabilize the roll, pitch, yaw angles?
Stability proof
Why can PID controller stabilize the quadrotor?
Summary
Notes: In the next lesson, we will revisit the PID controller.
We will see Why a PID controller can stabilize the quadrotor.
Also, we will make the attitude control.
So far, we’ve only learned the altitude control.
You will learn how to make the position tracking control in the next lecture.
That’s all from my side in the first lecture.

## Slide 32
10/17/2024
Ph.D. in Aeronautics and Astronautics
Shen
Thank you for
your attention
Notes: Thank you for your attention.
As far as I know, in today's lecture, there can be audiences at the beginner’s level.
So, I leave about 5 minutes for you.
Let me know if you have questions or comments.

## Slide 34
Research &
Teaching Concept
10/17/2024
Ph.D. in Aeronautics and Astronautics
Shen
Notes: In the following 10 minutes, I will talk about my research and teaching concept.

## Slide 35
I
1
Danish (Beginner)
English (Native)
Chinese (Mother Tongue)
Japanese (Medium)
Research
2017-2019
Birth
Master
(Technical University of Denmark)
Doctor
(The University of Tokyo)
2020-2023
1995
Notes: I’ll begin with my research.
This page lists some of my research publications during my doctoral program.
All of them are about robot simulator and robot control.
My primary contribution during my doctoral program was about the control theory and its application on the drones.

## Slide 36
I
The direction of the thrust is adjustable.
Ryll, Markus, Heinrich H. Bülthoff, and Paolo Robuffo Giordano. "Modeling and control of a quadrotor UAV with tilting propellers." 2012 IEEE international conference on robotics and automation. IEEE, 2012.
Tilt-rotor
4 magnitudes
4 tilting angles
Tiltrotor Dynamics
2
Research
Notes: The drone that I was focusing on during my doctoral program was called tiltrotor.
We introduced the tiltrotor in the trial lecture.
(play the demo)
There are 8 inputs in the tiltrotor.
They are 4 magnitudes of the thrusts and 4 directions of the thrusts.
We use a term called tilting angles to define the directions of the thrusts.

## Slide 37
I
Shen, Z. and Tsuchiya, T., 2022. Gait analysis for a tiltrotor: The dynamic invertible gait. Robotics, 11(2), p.33.
The direction of the thrust is adjustable.
Ryll, Markus, Heinrich H. Bülthoff, and Paolo Robuffo Giordano. "Modeling and control of a quadrotor UAV with tilting propellers." 2012 IEEE international conference on robotics and automation. IEEE, 2012.
Tilt-rotor
Tiltrotor Dynamics
where
3
Research
Notes: Here, we can see the dynamics of the tiltrotor.
The position and the attitude are governed by the 4 magnitudes and 4 directions of the thrusts, or we call them tilting angles.
My research focus was stabilizing the tiltrotor by feedback linearization.
Feedback linearization is a popular control method widely adopted in robotics.
I will brief the difficulties in applying feedback linearization from the next slide.

## Slide 38
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
Before the flight, roll and pitch are not determined.
Therefore, the gait will be designed based on the simplified determinant.
A gait, satisfying the simplified determinant, may still violate the original determinant.
where
4
Research
Notes: In applying feedback linearization, a singular decoupling matrix is not expected.
What you see here is the determinant of the decoupling matrix.
There are 6 variables in this determinant.
They are roll, pitch, and four tilting angles, alpha1, alpha2, alpha3, and alpha4.
To receive the invertible decoupling matrix, the determinant should be non-zero.
If we assign both roll and pitch zero, we receive a simplified determinant.
There are only 4 variables in the simplified determinant.
They are the tilting angles alpha1, alpha2, alpha3, alpha4.
In my research, these tilting angles are pre-defined by a user-defined procedure.
I created this procedure for the first time and called it Gait Plan.
Gait Plan determines the tilting angles alpha1, alpha2, alpha3, alpha4, in advance.
As we know, before the flight, neither roll nor pitch is determined.
Having no information about phi or theta, we cannot use the left formula.
Therefore, the gait (alpha1 alpha2 alpha3 alpha4) can only be planned based on this simplified determinant
Because we have no information about phi or theta in the left formula before the flight.
However, a gait, satisfying the formula on the right, may still violate the formula on the left.
This is because that rolls and pitches maybe non-zero.

## Slide 39
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
A gait, satisfying the simplified determinant, may still violate the original determinant.
5
Research
Notes: For example,
(play the demo)
this gait receives nonzero in the simplified determinant.
However, for some attitudes, the original determinant is zero.
Specifically, the rolls and pitches marked in blue in this figure result in the zero determinant.
These blue curves represent the unacceptable attitudes that lead to the singular decoupling matrix.
Traveling to the unacceptable attitude curves will result in the singular decoupling matrix, which is strictly prohibited.
Therefore, the attitude of the tiltrotor is only allowed to travel in a restricted way.
Here, the restricted way means traveling to the attitude not occupied by the unacceptable attitude curve.
Is there a way to enlarge the region of the acceptable attitude?
My research answered this question.

## Slide 40
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
Design a robust gait:
Let
where
6
Research
Notes: Since neither phi nor theta is determined, we expect a robust gait not influenced by roll or pitch.
In a robust gait, for any small roll or small pitch, the determinant is non-zero.
Here is how we find the robust gait.
Firstly, linearize the determinant at zero roll zero pitch.
The result yields:
The coefficient of phi times phi plus the coefficient of theta times theta plus the remaining term.
Since both phi and theta are uncertain in this problem, we assign both the coefficients of phi and theta zero.
By doing so, the contributions of the uncertain phi and theta are suppressed.
Further, to let the left side be nonzero, the remaining term should be nonzero.
The resulting gait is believed robust to the uncertain attitude.
So, we design the gait based on these 3 coefficients.

## Slide 41
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
7
Research
Notes: Following this method, I finally found a theorem called the Two color map theorem.
The Two color map theorem tells us how to design the robust gait, alpha1, alpha2, alpha3, alpha4.

## Slide 42
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
Gait 3
8
Research
Notes: This is the unacceptable attitude figure, as we introduced earlier.
It is a roll pitch diagram.
All the curves inside represent the attitudes that the tilt-rotor should not touch.
They are from 2 cases.
The red curves are the unacceptable attitudes if the tilt-rotor adopts the gait following the two color map theorem.
The blue curves are the unacceptable attitudes if the tilt-rotor adopts a gait not following the two color map theorem.
Clearly, the gait following the two color map theorem is more robust.
Because the red curves leave more space in the middle.

## Slide 43
I
Singularity in Attitude-Altitude Linearization in Tiltrotors
Gait 3
9
Research
Notes: As we mentioned, there are some singular attitude areas that the drone is not supposed to travel to.
Inspired by this, it is tempting to further this research domain with the control barrier function.
Control barrier function, also known as CBF, is a useful tool to restrict the controlled object with some constraints.
Here, the constraint is the singular attitudes.
Also, the CBF can be used to avoid the input constraint in my controller.
I am motivated to play with them.

## Slide 44
10
I
Research
Notes: From the next month, I will join a research project with EUROfusion.
It is to control a robotic arm for the nuclear fusion.
To avoid the collision between the robotic arm and the equipment of the reactor, the control barrier function is equipped.
So, I will also make a deep investigation into the control barrier function with the model of the robotic arm.
Those are my research interests.

## Slide 45
11
II
Teaching Concept
Write the complicated formula directly?
Notes: As for my teaching concept.
I never think it is a good idea to put down the complicated formula directly in my class.
I always pretend that I am also a student learning the knowledge for the first time.
As a student, I don’t like seeing the complicated formula directly.
Without the explanation, it would be a headache.
So, I do not support give lectures by simply putting down the formulas.

## Slide 46
12
II
Teaching Concept
Class for everyone.
able to follow
for advanced researchers
Notes: Instead, I will make the necessary deduction with the students.
I understand that students may have different prior knowledge.
By deducing step by step, the beginners can also follow the whole picture.
The advanced researchers, on the contrary, will also benefit from the deducing process.
It will sometimes give the inspiration for his or her research.
The mathematical deduction can sometimes be transplanted maybe from the most basic and simplest knowledge.

## Slide 47
13
II
Teaching Concept
Play with it!
The Altitude of The Quadrotor
https://github.com/HansOersted/trial_lecture
The program is provided on GitHub.
Notes: At last, I encourage the students to play with the simulator.
When learning a new control algorithm, the best way can be playing with it.
So, I make my controller open-source on GitHub.
The students can clone and play with it while learning.
This simulator can be used beyond the educational purpose.
There can be young researcher interested in this domain.
They can build their own controller in this simulator and make publications.

## Slide 48
II
14
First Page
Notes: Let me conclude this presentation.
This is the first page of my doctoral thesis.
I put this sentence here because:
I hope every student coming to Austria from different countries, starting at different levels, can always enjoy and learn something from my lecture.

## Slide 49
Shen
Thank you for
listening
Ph.D. in Aeronautics and Astronautics
10/17/2024
Notes: Thank you for your listening.
This is the real end of my presentation.